Author: Adrian Szklarski, 07.06.2022.
Technological level: Intermediate
Programming level: Junior +
Technologies used: Python 3.10 | PyCharm | Linux | OpenOffice

Description of the problem: The single-stage space rocket is propelled by liquid hydrogen and oxygen, while the propellants of the two two-stage rockets are LH-LOX (liquid oxygen and hydrogen) and kerosene, respectively. The masses of the rockets should be compared. Then compare the velocity increments of the single-stage rocket and the three-stage rocket under the assumptions:
1. total mass the same for both rockets;
2. the specific impulse is the same for both rockets;
3. design factors the same for both rockets;
4. I Space velocity:	V_I =7785 m / s
5. Loss of speed:	ΔV_loss = 2056 m/s
6. Payload weight:	m_pw=1285 kg
7. Construction factor:	ε = 0.08

Solving the task:

Single-stage rocketLH2-LO2
Exhaust gas velocity:	w = 4500 m/s
Total speed increase:	ΔV = V_I + ΔV_loss

weight of construction: m_w = m_pw {(x-1)} over {1+ {1} over {ε} -x} , x = e^(Δv/w)
fuel weight:	m_f = { m_{w} } over {ε}
gross weight:	m_g1 = m_w + m_f

Two-stage rocketLH2-LO2
Exhaust gas velocity:	w = 4500 m/s
Total speed increase:	ΔV_{I}= {ΔV} over {2} , ΔV_{II}= {ΔV} over {2}
Second stage:

x_{II2} = e^( Δv_{II} /w) , m_{II2} = m_{pw} , m_KII = m_II2 {( x_{II2} -1)} over {1+ {1} over {ε} - x_{II2} } , m_fII = { m_{KII} } over {ε} , m_gII = m_KII + m_fII
First stage:

x_{I1} = e^( Δv_{I} /w) , m_{I1} = m_{pw} + m_{qII} , m_KI = m_I1 {( x_{I1} -1)} over {1+ {1} over {ε} - x_{I1} } , m_fI = { m_{KI} } over {ε} , m_gI = m_KI + m_fI

Two-stage rocketkerosene_LO2
Exhaust gas velocity:	w = 3200 m/s
Total speed increase:	ΔV_{I}= {ΔV} over {2} , ΔV_{II}= {ΔV} over {2}

Second stage:

x_{II2} = e^( Δv_{II} /w) , m_{II2} = m_{pw} , m_KII = m_II2 {( x_{II2} -1)} over {1+ {1} over {ε} - x_{II2} } , m_fII = { m_{KII} } over {ε} , m_gII = m_KII + m_fII
First stage:

x_{I1} = e^( Δv_{I} /w) , m_{I1} = m_{pw} + m_{qII} , m_KI = m_I1 {( x_{I1} -1)} over {1+ {1} over {ε} - x_{I1} } , m_fI = { m_{KI} } over {ε} , m_gI = m_KI + m_fI
Summary:

Conclusions:
1. A two-stage rocket has less mass for the same speed gain;
2. A rocket powered by liquid hydrogen and oxygen is lighter than the same rocket powered by kerosene and liquid oxygen